## Slide 1: FoSTERing Restoration Success at Cuyahoga Valley National Park
Christie Bahlai (Biological Sciences)
Chris Blackwood (Biological Sciences)
Anne Jefferson (Geology)
Notes: Acknowledge funding sources: Kent State Department of Geology; Kent State Graduate Student Senate; the Geological Society of America; and the Geoscientists-in-the-Parks Program

## Slide 2
FoSTERing Reforestation
Park Goal: reforest mine sites
Cuyahoga Valley National Park established in 2000
Cuyahoga Valley used for farming, industry, & mining
Kent State is science partner
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 3
1950s – 1990s
Slope cut backwards as
sand and gravel was quarried
Snowville Quarry
Photo: CUVA Division of Resource Management
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 4
1950s – 1990s
Slope cut backwards as
sand and gravel was quarried
1999
Site is graded, compacted
and seeded
Snowville Quarry
Photo: CUVA Division of Resource Management
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 5
1950s – 1990s
Slope cut backwards as
sand and gravel was quarried
1999
Site is graded, compacted
and seeded
2001
Planted 1125 tree seedlings. They all died.
Snowville Quarry
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 6
1950s – 1990s
Slope cut backwards as
sand and gravel was quarried
1999
Site is graded, compacted
and seeded
2001
Planted 1125 tree seedlings. They all died.
Snowville Quarry
September 2018
Site is deep-ripped
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 7
1950s – 1990s
Slope cut backwards as
sand and gravel was quarried
1999
Site is graded, compacted
and seeded
2001
Planted 1125 tree seedlings. They all died.
Snowville Quarry
September 2018
Site is deep-ripped
September 2018 – Current
Native tree saplings are being
planted in the cross-rips
Notes: CUVA decided to put this reclamation plan into action in 2016, starting with a topsoil mine known as Dover.
During the 1990s, the top 3 m of topsoil were removed from Dover for construction of a ski slope. Shortly afterward, the mine was reclaimed in accordance with SMACK-RA. It was backfilled with dredged sediment and leftover soils from a parking lot construction.
In 2012, in an attempt to return Dover to a native forestland, CUVA planted approximately 1200 native tree seedlings. By 2016 over 95% of the seedlings had died. Inspection of the seedlings led CUVA staff to believe that root constriction was the cause.
While Dover is the only site that CUVA has attempted to plant without further reclamation, it is one of five sites that are currently slated for reforestation.
We have started studying the soil properties on the sites that were reclaimed under SMACK-RA guidelines and how those properties change with deep-ripping.

## Slide 8
A bulldozer with plow-shaped shanks
rips the site in a cross-hatch pattern
Tilling the soil reduces soil compaction
Reduced soil compaction and rough
microtopography increases water
infiltration and rooting
Deep-Ripping Reclamation
Notes: One approach in reclaiming these surface mines is a process referred to as “deep-ripping,” “deep-tillage,” or “subsoiling.”
After invasive plants are removed from a site (often through a combination of herbicide application and mowing), a bulldozer with meter-long shanks will make passes over a surface mine to rip up the soil in a fashion similar to tilling. In clay-rich environments, a plow-shaped shank is used and the bulldozer rips in a cross-hatch pattern to better rupture the surface of the soil and prevent trenching during precipitation events.
This process of deep-ripping is meant to reduce soil compaction and ultimately promote infiltration and rooting. Trees can then be planted at the intersection of these rips, where the roots can branch out in four directions to take advantage of the reduced soil compaction, increased infiltration, and reduced invasive plant competition.

## Slide 9: Science Questions, Part 1: What’s wrong?
How do the mine sites differ from un-mined soils and ecosystems?
  Catherine Ruhm, MS, 2018
  On-going and completed data collection by Blackwood lab

## Slide 11
Surface bulk density isn’t so much the problem as what happens below 5 cm.
Soils become too dense for roots.

## Slide 13: Science Questions, Part 2: How does restoration change things?
How does deep-ripping affect soil properties, hydrology, and ecosystems?
  Data on hydrology/soil physical properties for 1 site (Dover) in Ruhm MS thesis.
  On-going soils/hydrology data collection at site 2 (Snowville). This is where you come in.
  Biologists are doing stuff too.

## Slide 15: Science Questions, Part 3: What happens next?
How do different mycorrhizae and trees change the soil, hydrology, and ecosystem?
  First we need to keep the trees alive!

## Slide 16: Science Questions, Part 2: How does restoration change things?
How does deep-ripping affect soil properties, hydrology, and ecosystems?
  Data on hydrology/soil physical properties for 1 site (Dover) in Ruhm MS thesis.
  On-going soils/hydrology data collection at site 2 (Snowville). This is where you come in.
  Biologists are doing stuff too.

## Slide 17: Soil moisture
Surface runoff
Topography

## Slide 18: Weather Station
Adfadf
https://hobolink.com/p/2a35b5e2fc23e20c9d7388c41a31f8fb
Temperature
Rain (mm)

## Slide 19: 2 months pre-rip (2018) 1 year post-rip (Sept 2018-present)

## Slide 20: How does ripping affect soil moisture?
Pre-rip vs. post-rip
Slope vs. flat portion of site
No-rip vs. single rip vs. cross-rip (intersection of rips)
Seasonal (but weather is different)
Response to precipitation inputs (using weather station data)
Slope

## Slide 21: How does ripping affect soil moisture?
Pre-rip – slope
  20 cm
  50 cm
Pre-rip – flat
  20 cm
  50 cm
Slope
Flat

## Slide 22: How does ripping affect soil moisture?
Post-rip – slope
  10 cm cross-rip
  10 cm EW rip (slope parallel)
  10 cm NS rip (up-down slope)
Post-rip – flat
  10 cm cross-rip
  20 cm no rip
Slope
Flat

## Slide 23: Supporting data (later in semester?)
Bulk density – top 5 cm (pre- and post-)
Bulk density profiles near soil moisture sites (pre- and post-)
Saturated hydraulic conductivity (pre- and post-)
Advanced topic: topographic change!

## Slide 24: Participatory Science
Recruitment of volunteers at planting events

## Slide 25: Participatory Science
Trial run of “Spot the Ladybug”
New event- The CVNP Beetle blitz!

## Slide 26: 3. The website
https://foster-project.org
Beta testing Google forms/sheets as data entry system, but running into limits
Exploring alternative data management software suites

## Slide 27: 4. Education
Volunteers for participatory science recruited (summer, fall 2018 plantings)
Additional volunteers to be recruited (spring 2019 plantings)
Pre/post-test for volunteers, under development
  Noticing skills (qualitative notes, details in environment)
  Insect identification skills
  Measuring skills (trees)
Training for volunteer trainers, under development

## Slide 28: Future Funding Strategy
KSU student placed as Geoscientist-in-the-Park
Dominion Energy Foundation proposal, April 2018
NSF Research Coordination Network proposal, November 2018
Cooperative Ecosystem Studies Unit proposal, December 2018
NSF Macrosystems proposal in progress for February submission, “incidental tick capture.”
More submissions planned

## Slide 29
A bulldozer with plow-shaped shanks
rips the site in a cross-hatch pattern
Tilling the soil reduces soil compaction
Reduced soil compaction and rough
microtopography increases water
infiltration and rooting
Deep-Ripping Reclamation
Notes: One approach in reclaiming these surface mines is a process referred to as “deep-ripping,” “deep-tillage,” or “subsoiling.”
After invasive plants are removed from a site (often through a combination of herbicide application and mowing), a bulldozer with meter-long shanks will make passes over a surface mine to rip up the soil in a fashion similar to tilling. In clay-rich environments, a plow-shaped shank is used and the bulldozer rips in a cross-hatch pattern to better rupture the surface of the soil and prevent trenching during precipitation events.
This process of deep-ripping is meant to reduce soil compaction and ultimately promote infiltration and rooting. Trees can then be planted at the intersection of these rips, where the roots can branch out in four directions to take advantage of the reduced soil compaction, increased infiltration, and reduced invasive plant competition.